## Slide 1
What is computer Programming?

## Slide 2
Computer Programming Definition
Computer programming is a way of giving computers instructions and tell them what to do next!

## Slide 3
How Computers Work!
Process
Storage
Output
Input
Program
Computers main functions:

## Slide 4
How Computers Work!
Computers are machines that perform mathematical operations on numbers using electronic voltage.
Example: Image Processing:
Example: Sound Processing:

## Slide 5
How Computers Work!
Let’s make a computer using electrical voltage to do mathematics:
+ =
2
5
3
+ =
3000
3003
3
+ =
2.75
5.95
3.2
Problem I: Scale
Problem II: Precision
Loss
2.00 V
3.00 V
3000.00 V
3.00 V
2.75 V
3.2 V

## Slide 6
So What is the solution?
+ =
01101
100110
11001
How Computers Work!
1 Volt
0 Volt
1 Volt
0 Volt
Problems:
We need new system of counting using only 1 and 0
We need new algebra for doing math in this new system
Binary System

## Slide 7
Decimal:
1x +3x+6x +1x
In Decimal System we have 10 symbols:
So decimal is a positional numeral system in which each position has positional notation of 10:
 |  |  |  | 1 | 3 | 6 | 1
 |  |  |  | 1 | 3 | 6 | 1
1+300+60+1
1361

## Slide 8
Binary:
1x + 1x + 0x + 1x + 1x + 1x
In Binary System we have 2 symbols:
So Binary is a positional numeral system in which each position has positional notation of 2:
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1x128+1x64+0x32+1x16+1x8+0x4+1x2+1x1
129

## Slide 9
Lets complete our computer prototype:
+ =
01101
100110
11001
Computers are machines that perform mathematical operations on numbers using electronic voltage.
To create this voltage with reasonable speed we use a electronic element called transistor
Transistor can either be ON or OFF and can be switched On and off with very small voltage.
OFF
ON

## Slide 10
Transistors:

## Slide 11
CPUs and Memories:
3 billion Transistors
8 billion Transistor in 1G
+ =
01101
100110
11001
Store Binary Value
Perform Mathematic operation
For adding two digits, using transistors, our computer should perform below functions:
RAM:
Random Access Memory
CPU:
Central processing Unit

## Slide 12
Random Access Memory:
Capacity: 16 Byte
16 Memory Location
Each Memory location=8 Bit
16x8=128 Bit=16 Byte
Instructions
Data
Control Bits

## Slide 13
CPUs Function:
Instructions
Data
CPU
1:Fetch Instruction
Description | Control Bits
Get number in Memory Location 12 | 10011001
Get number in Memory Location 13 | 10001111
ADD Numbers in location 12 and 13 | 00011001
STORE in Memory Address 14 | 10001110
2:Decode Instruction
Execute
DATA BUS
3:Execution
Decode
Execute
Fetch
Intel Core i7 clock rate is around 4 GHz, this means it executes 4 billion cycles per second
CPU Clock is used to synchronize the operations of CPU components. It is an indicator of the processor's speed.
It is measured in clock cycles per second or its equivalent, hertz (Hz).
A CPU with a clock rate of 1 Hz executes 1 cycles per second.

## Slide 14
What is computer Programming?
Basically Programming is loading instruction and data to Ransom access Memory(RAM)
Description | Control Bits
Get number in Memory Location 12 | 10011001
Get number in Memory Location 13 | 10001111
ADD Numbers in location 12 and 13 | 00011001
STORE in Memory Address 14 | 10001110
In early years of programming, programmers would use binary control Bits to program. They were using instruction table to find correct control bit.
In 1947 “Kathleen Booth” Created Assembly language
Assembly Syntax (OPCODE) | Description | Control Bits
Load_A | Get number in Memory Location 12 | 10011001
Load_B | Get number in Memory Location 13 | 10001111
ADD | ADD Numbers in location 12 and 13 | 00011001
STORE | STORE in Memory Address 14 | 10001110

## Slide 15
What is computer Programming?
“Kathleen Booth” Created a program to translate OPCODES to Control Bits
OPCODE
01101101
Assembler
Assembly is low level programming language. Each OPCODE is corresponding with one control Bit.

## Slide 16
What is computer Programming?
In 1959 “Grace Hopper” invented first programming language called COBOL(COmmon Business-Oriented Language)
Compiler
LOCAL-STORAGE SECTION.
01 LS-CLASS PIC 9(3)
0101111000110110100100111001001001000100100100010011111110000001111000011110101001111111001111111111100000111111111
Hopper created a program which was translating Syntaxes to Binary Code.
Each COBOL syntax would execute several control Bits

## Slide 17
Programing Languages
Low Level Languages
High Level Languages
Machine Language
Assembly Language
1991
1972
1980
1991
1994
1945

## Slide 18
Algorithm
Algorithm is a set of step-by-step instructions, placed in a right order to make something useful happen.
Take lid off the toothpaste
Spit and rinse the brush
Brush teeth for 2 minutes
Squeeze toothpaste on the brush
Run Water onto the brush
If temperature is less than 10 degrees
If temperature is greater than 18
Wear Jumper
Wear Coat
If temperature is between 10 and 18
Wear T-shirt
Brushing Your Teeth
Choosing what to wear!

## Slide 19
Algorithm
Which Number is the largest?
13
9
19
20
4
25
12
6
23
17
24
25

## Slide 20
Algorithm
Look at the first number on the screen. Remember it. Store it in your brain
Look at the next number
Question:
Is it larger than what you remembered?
YES!
NO!
Forget that number and keep remembering the previous one.
Remember that one!

## Slide 21
What is computer Programming?
Computer programming is a process of designing and building executable instructions based on algorithms to accomplish a specific computing result or to perform a specific task.
Analyzing
Generating Algorithm
Translate Algorithm to Programming Language
Programming Process: